## Slide 1: EcoBot: The Smart Garbage Collection Robot
Muhammad yasser alali
200047921
Dr. Mohammed Marei Eng. Ahmed Abdellatif

## Slide 2
Introduction & Objective
What is the project?
"EcoBot" is a prototype of a wireless-controlled mobile robot, equipped with a 4-Axis Robotic Arm.
How does it work?
The robot is fully controlled (for both movement and the arm) using PS5 controller via Bluetooth.
The Goal?
The objective is to provide a technical solution to help preserve the environment by designing an automated (smart) system capable of collecting waste and garbage from public spaces.

## Slide 3
Hardware Components:
Main Controller:
ESP32 Board (for Bluetooth and logic control).
Robotic Arm:
4 Servo Motors (Base, Shoulder, Elbow, Gripper)
PCA9685 16-Channel Servo Driver (for precise control via I2C).
Robot arm

## Slide 4: Hardware Components:
Drive System:
4 DC Motors (wired as pairs).
L298N Motor Driver.
Power System:
Main Battery (11V LiPo): Powers the Motors (L298N) and the ESP32.
Secondary Battery (7.4V): Powers the Servo Driver (PCA9685) only.
Buck Converter: Steps down the main 7.4V to a clean 5V for the ESP32 and L298N logic.

## Slide 5
Control System:
Hardware Components:
PS5 Controller: Just for operating experience
Chassis:
Custom-built wooden chassis.

## Slide 6
System Architecture:
Power Distribution:
  11V Battery → Feeds the L298N (VMS) and the Buck Converter (IN).
  7.4V Battery → Feeds the PCA9685 (V+) (Servo power).
  Buck Converter (5V OUT) → Feeds the ESP32 (5V), the L298N (5V Logic), and the PCA9685 (5V) (Logic power).
Common Ground (GND):
  All GNDs (Both Batteries, Buck, ESP32, L298N, PCA9685) must be connected together.
Control Signals (ESP32):
  L298N (Left): GPIO 16, 17, 18 .
  L298N (Right): GPIO 5, 13, 14 .
  PCA9685 (I2C): GPIO 4 (SDA), 15 (SCL).

## Slide 7
Software & Technologies
IDE: Arduino IDE (C++).
Board Package:
  esp32_bluepad32 (Required for stable PS5 controller support).
Wireless Control:
  Bluepad32 Library (Connects to PS5 and handles virtual devices).
Motor Control (L298N):
  ledcSetup/ledcAttachPin for precise PWM speed control (at 5KHz).
Arm Control (PCA9685):
  Wire.h (I2C Protocol).
  Adafruit_PWMServoDriver Library (Manages all 16 servo channels).
Code Logic:
  An adaptive vTaskDelay(active ? 1 : 5) logic to balance responsiveness and system stability.

## Slide 8
Control Logic:
Vehicle Movement:
  Forward (Variable Speed): Left Joystick (Up)
  Backward (Variable Speed): Left Joystick (Down)
  Spin Left (Fixed Speed): Triangle Button (△)
  Spin Right (Fixed Speed): Circle Button (○)
Robotic Arm:
  Base (Left/Right): L2 / R2
  Shoulder (Up/Down): Right Joystick (Up/Down)
  Elbow (Forward/Back): L1 / R1
  Gripper : Open ( □ ) / Close ( X )

## Slide 9
Code Structure Summary
Core Functions:
  setup() – Initializes hardware (motors, servos, Bluetooth).
  loop() – Runs continuously, handles input and logic.
Main Logic Function:
  control(ControllerPtr ctl) – Reads controller input and calls helper functions.
Helper Functions:
  motor(left, dir, spd) – Controls robot motors (L298N).
  servo(ch, ang) – Controls a servo via PCA9685.
Bluetooth Callbacks:
  onConnect(ctl) – Triggered when a controller connects.
  onDisconnect(ctl) – Triggered when a controller disconnects.

## Slide 10
Challenges Faced
1. Initial Hardware Failure:
  We faced the failure of two ESP32 boards at the start of the project due to incorrect power wiring and attempts to use an L293D shield.
2. L293D Driver Incompatibility:
  We discovered the L293D shield was defective (M1/M2 channels were dead) and used a complex (Shift Register) control system.
  Solution: Replaced it with the simpler and more robust L298N driver.
3. Bluetooth Connectivity Issues:
  Difficulty connecting Bluepad32 due to experimenting with other (incompatible) Bluetooth libraries, which led to a Core Software Conflict in the Arduino IDE.
  Solution: The solution was to switch libraries.

## Slide 11
Results & Demo
Current Status:
  A fully functional prototype.
  The robot connects reliably to the PS5 controller.
  All systems (Movement and Arm) respond correctly to the new control scheme.
  The "dual-voltage" power system successfully isolates motor noise from the logic circuits.
Live Demonstration:
  (Click to watch the video)

## Slide 12
Future Operations:
1. Standalone Mode (AI):
  Integration of an ESP32-CAM vision camera.
  AI/Machine Learning training model (using tools such as Edge Impulse) on:
    Object Detection (detecting objects).
    Waste Sorting (distinguishing between plastic, paper, and metal).
2. Mechanical Improvements: (Corrected from "Pricing")
  Design and printing of a custom, lightweight frame and use of high-quality components.

## Slide 13
Thank you for your attention